| APPLICATION ENGINEERING | CUSTOMER DESIGN CRITERIA | 1-Week delivery is based upon receipt of this completed document at D-M-E. |
| --- | --- | --- |
| AE004.14 | 06-20-05 | *BLUE AREAS ARE FOR DME USE ONLY* |  |
| CUSTOMER NAME: | DATE | ACCOUNT # | SHOP ORDER #: |
| CONTACT NAME: | PHONE # | FAX # | DELIVERY DATE: |
| DME STAT # | QUOTE # | P.O. # | JOB # | MATERIAL GENERIC NAME: BRAND NAME: FILLER: PROCESS TEMP: F° C° |
| MANIFOLD KIT PLUS CATALOG #: | CUSTOMER EMAIL ADDRESS: |  |
| METEOR-2 CENTER EXIT MANIFOLD Vertical flow diameter machined, end plug and set screw installed. ‘DL’= |
| Return completed form to D-M-E Company – Madison Heights, MI. email address: dme@appl_eng.net fax #: 248-544-5707 See page 2 for available manifold sizes. |

| METEOR-2 CENTER EXIT MANIFOLD MANIFOLD SELECTION CHART |
| --- |
| MANIFOLD KIT PLUS CATALOG # | NOZZLE SERIES | NL-MIN | NL-MAX | OAL | V-vertical flow diameter |
|  |  | MM | INCH | MM | INCH | MM | INCH | MM | INCH |
| MCM0100KP | 250 EHA 250 CIA Mini Gate-Mate Gate-Mate 4 | 55 | 2.165 | 100 | 3.937 | 195 | 7.677 | 9 | 0.354 |
| MCM0150KP |  | 100 | 3.937 | 150 | 5.906 | 245 | 9.646 |  |  |
| MCM0200KP |  | 150 | 5.906 | 200 | 7.874 | 295 | 11.614 |  |  |
| MCM0300KP | 375 EHA 375 CIA Gate-Mate 4 | 200 | 7.874 | 300 | 11.811 | 395 | 15.551 | 12 | 0.472 |
| MCM0400KP |  | 300 | 11.811 | 400 | 15.748 | 495 | 19.088 |  |  |
| MCM0500KP |  | 400 | 15.748 | 500 | 19.685 | 595 | 23.425 |  |  |
| These systems are designed to operate on a 240 volt, 3 phase supply NOTE: See Meteor system assembly guide for installation details. The above chart is for reference purposes only |

# Text boxes

OAL

‘V’  VERTICAL FLOW DIA.

NOTE:

Sheet #1 MUST be completely filled out and returned to D-M-E in order to proceed.

NOTE TO CUSTOMER: This form contains a series of gray text fields and check boxes. Please click in each field and enter the required data or make a selection from the options shown. Email back to sender once you are complete. This will keep the verification and design process moving forward.

NOZZLE PLATE

# ‘NL’ MIN

# ‘NL’ MAX

The vertical flow channel ‘V’ location will be calculated by D-M-E based on the customer’s ‘DL’ dimension and the material process temperature.

‘DL’ equals the distance from the centerline of the mold to the actual drop/gate location in the mold.